A & B is the power in 12VDC.  This activates the coil which in turn pulls contacts 3 & 5 and 4 & 6 together.  When there is no power contacts 1& 5 are together and 2 & 6 are together.  So you would hook your incoming line to 5&6.  The line to your asterisk server on 3&4. and a line going to the jack in your house on 1&2.  This won’t hurt to have the line hooked to the same jacks as the FXS port because the POTS dial tone will only be there when the server is powered off.